A Synchronous Operating System for Reactive Applications
(i.e., OS following the concurrency model of Céu)

---
Motivations
Specific demands
  - Micro platforms
    - 4MHz, (32+4)Kb
  - Multiple platforms
    - Arduino, WSNs
    - Peripherals
  - Remote reprogramming
General frustrations
  - “Programmability”
    - select? Really?
    - Threads? Really???
  - Complexity
    - preemptive scheduler
    - per-process resources
  - Safety
    - non-deterministic
      execution

---
Specs
- Micro-kernel architecture
  - Scheduler + IPC (11 system calls so far // Linux has ~200)
- Scheduler
  - Deterministic = Reproducible + Predictable
  - Single stack + queue shared by all processes
- IPC through events/calls
  - Typed output => input
  - Dynamic/decoupled linking

---
DEMO 1: shell + 2 “apps”
6 processes: 14336 (text) + 1039 (data+bss)

---
DEMO 2: GPIO driver + app
output (u8,u8)=>void PIN_MODE;
output (u8,u8)=>void DIGITAL_WRITE;
input (u8,int) DIGITAL_CHANGED;
call PIN_MODE => (13,_OUTPUT);
call PIN_MODE => ( 2,_INPUT);
var int dt = 1000;
par do
    loop do
        call DIGITAL_WRITE => (13,_HIGH);
        await (dt)ms;
        call DIGITAL_WRITE => (13,_LOW);
        await (dt)ms;
    end
with
    loop do
        var u8 pin;
        var int v;
        (pin, v) = await DIGITAL_CHANGED
        until pin == 2;
        if dt > 100 then
        dt = dt - 50;
        end
        await 200ms;
    end
end
input (u8,u8)=>void PIN_MODE;
input (u8,u8)=>void DIGITAL_WRITE;
output (u8,int) DIGITAL_CHANGED;
var u16 pins_m = 0xFFFF; // all OUTPUT
var u16 pins_v = 0x0000;
input (u8 pin, u8 mode)=>void PIN_MODE do
   _pinMode(pin, mode);
   _bitWrite(this.pins_m, pin, mode);
end
input (u8 pin, u8 val)=>void DIGITAL_WRITE do
   _digitalWrite(pin, val);
end
every 50ms do
   loop i, 14 do
      if _bitRead(pins_m,i) == _INPUT then
        var int v = _digitalRead(i);
        if v != _bitRead(pins_v,i) then
        _bitWrite(pins_v, i, v);
        emit DIGITAL_CHANGED => (i,v);
        end
      end
   end
end

---
Inter-process comm.
Events:
- enqueued / deferred
- no pointers as parameters, cannot return values
- “distributable”
- N => N (including 0)
  (N emit sources may trigger 1 await sink)
  (1 emit source may trigger N await sinks)
Calls:
- immediate execution
- pointers as parameters, can return values
- local only
- N => 1 (excluding 0)
  (N call sources may trigger 1 definition)
  (1 call source may trigger 1 definition)
- (!!!) Recursive definitions

---
Safety: Recursive calls
- Breaks the synchronous model
- Solutions:
  1. Call definitions cannot make any other calls.
  2. Call definitions carry their dependencies, then at link time build and check the “call graph” (ceu_sys_link may fail).
  3. A call/rec syntax for recursive calls.

---
Safety: Finalization
Programs are enclosed by await OS_STOP
par/or do
   #include "gpio.h"
   output (u8,u8)=>void PIN_MODE;
   output (u8,u8)=>void DIGITAL_WRITE;
   call PIN_MODE => (11,_OUTPUT);
   finalize with
      call DIGITAL_WRITE => (11,_LOW);
   end
   loop do
      call DIGITAL_WRITE => (11,_HIGH);
      await 1s;
      call DIGITAL_WRITE => (11,_LOW);
      await 1s;
   end
with
   await OS_STOP;
end
#include "gpio.h"
output (u8,u8)=>void PIN_MODE;
output (u8,u8)=>void DIGITAL_WRITE;
call PIN_MODE => (11,_OUTPUT);
finalize with
   call DIGITAL_WRITE => (11,_LOW);
end
loop do
   call DIGITAL_WRITE => (11,_HIGH);
   await 1s;
   call DIGITAL_WRITE => (11,_LOW);
   await 1s;
end

---
OS internals: System calls
void ceu_sys_start (tceu_app* app);
void ceu_sys_stop (tceu_app* app);
void ceu_sys_link (tceu_lnk* lnk);
void ceu_sys_unlink (tceu_lnk* lnk);
int ceu_sys_emit (tceu_app* app, u8 evt, tceu_p param, int sz, char* buf);
tceu_p ceu_sys_call (tceu_app* app, u8 evt, tceu_p param);
void ceu_sys_scheduler (void);
tceu_queue* ceu_sys_dequeue (void);
void ceu_sys_go_event (tceu_app* app, int id, tceu_p data);
void ceu_sys_go_async (tceu_app* app);
void ceu_sys_go_wclock (tceu_app* app, s32 dt);

---
OS internals: The scheduler
void ceu_scheduler (void) {
tceu_app* app;
    tceu_lnk* lnk;
    while (1) {
app = CEU_APPS;
        int _dt = CEU_DT();
        for (; app; app=app->nxt) {
        ceu_sys_go_wclock(app, _dt);
        if (! app->isAlive)
        ceu_sys_stop(app);
        }
app = CEU_APPS;
        for (; app; app=app->nxt) {
        ceu_sys_go_async(app);
        if (! app->isAlive)
        ceu_sys_stop(app);
        }
        tceu_queue* qu = ceu_sys_dequeue();
        if (qu != NULL) {
        lnk = CEU_LNKS;
        for (; lnk; lnk=lnk->nxt) {
        if (qu->app!=lnk->src_app || qu->evt!=lnk->src_evt)
        continue;
        ceu_sys_go_event(lnk->dst_app, lnk->dst_evt, qu->param);
        if (! lnk->dst_app->isAlive)
        ceu_sys_stop(lnk->dst_app);
} } } }

---
A Synchronous Operating System for Reactive Applications
(i.e., OS following the concurrency model of Céu)

---
Next
- Zero-copy events
  - ex. packets
- Requests
  - in between a call and event
  - example, request a line from serial
  - requires the callee to hold state to the caller
  - emit must be paired with await, but across multiple reactions

---
Some definitions
- Operating System
  - An operating system (OS) is a collection of software that manages computer hardware resources and provides common services for computer programs. [wikipedia]
- Process
  - xxx
- Micro kernel
  - xxx