Structured Synchronous Programming with Céu
(a data-oriented perspective)
Francisco Sant'Anna
www.ceu-lang.org

---
Synchronous Programming
- Real-time/continuous interaction with the environment
  - I/O, sensor/actuators
- Two approaches (early 80s in France):
  - Control oriented (imperative): Esterel
  - Data oriented (functional/declarative): Lustre/Signal
- Global/external notion of time (e.g., clock ticks)
- Synchronous hypothesis
  - “Reactions execute infinitely faster in comparison to the input rate.”
- The synchronous model requires asynchronous primitives
  - take time and execute across reactions (e.g., network communication, heavy computations, etc.)

---
Synchronous Programming
- Esterel
  - Control dependency
  - Imperative statements
  - Reactive to the environment
    - Program counter
      - Synchronous: one input at a time
- Lustre
  - Data dependency
  - Equations/Combinators
  - Reactive to the environment
    - Graph traversal
      - Synchronous: complete traversal
Environment
Input
Output

---
Synchronous Programming
Can we cross this line?
Can we reconcile control and data-oriented
 synchronous programming?

---
“Hello world!” in Céu
Blinking a LED
  1. on ↔ off every 500ms
  2. stop after “press”
  3. restart after 2s
- Compositions
  - seq, loop, par (trails)
    - At any level of depth
  - state variables / communication
    par/or do
       loop do
        await 500ms;
        _leds_toggle();
       end
    with
       await PRESS;
    end
 loop do
    par/or do
       loop do
        await 500ms;
        _leds_toggle();
       end
    with
       await PRESS;
    end
    await 2s;
 end
       loop do
        await 500ms;
        _leds_toggle();
       end
Lines of execution
=
Trails (in Céu)

---
Design guidelines / Tradeoffs in Céu
(vs data streams/signals + functional combinators)
(vs ???)
(vs garbage collection)
(vs purity / immutable data)
(vs “free parallelism”)
- Control flow
  - explicit state machines (fold combinator)
- Structured programming
- Bounded execution and memory
- Automatic memory management (lexical scope + safe abortion)
- Side effects everywhere
- Sequential/Deterministic semantics (real parallelism relies on asynchronous primitives)
- Data flow
  - explicit loops with side effects
crossing the line

---
Mixing data & control
- Controlling the ball inside a rectangle
  - click the mouse to start
  - click the mouse to turn right (always)
- Data flow:
  - velocity is the integral of acceleration
  - position is the integral of velocity
- Control flow:
  - abrupt changes in the edges (non-continuous functions)
  - discontinuity imposes state machines (e.g., isRunning, curDirection)

---
Moving the ball
- Ugly, lengthy, low level!
  - simple data dependency pattern
    - 1 par + 2 loop
- Abstractions
  - Organism = Object + Trails
    - Interface (fields + methods)
    - Body (any code in Céu)

---
Moving the ball
- Organisms
  - constructor starts the body to execute in parallel with the remaining block
- Still verbose
  - Local transformations only
  - Syntactic sugar

---
Making the turn
- Doesn't work as expected
  - previous dependency still active
- Lexical scope for organisms
  - data reclaimed, body aborted
- Mixing data and control flow
  - automatic data updates
  - no explicit state machines or resets
  - structured code with lexical scope

---
Closing the loop
- Lenghty code...
  - ... but regular
  - “abstractable” with macro or class

---
Closing the loop
Structured, sequential, and with encapsulated data flow.

---
References
- “Real Time Programming: Special Purpose or General Purpose Languages” - G. Berry (1989)
  - synchronous model, interactive vs reactive systems
- “Preemption in Concurrent Systems” - G. Berry (1993)
  - safe abortion, Esterel semantics
- “Safe Concurrent Abstractions for Wireless Sensor Networks” - (SenSys'13)
  - static Céu, constrained platforms (8bit CPU, 4K RAM)
- “Structured Synchronous Reactive Programming with Céu” - (Modularity'15, FPW/StrangeLoop'14)
  - dynamic Céu, abstractions with lexical scope

---
Recursive data structures
- Interpreter for a simple Logo turtle
  - move N pixels
  - rotate N degrees
  - sequence, repetition
- Program as an abstract syntax tree (AST)
  - sequence and repetition are recursive
ongoing / unpublished work

---
Recursive data structures

---
Structured Recursive Loops

---
A more powerful Turtle
- Interpreter for a powerful Logo turtle
  - move N pixels per second
  - rotate N degrees per second
  - await N milliseconds
  - sequence, repetition, par/or

---
A more powerful Turtle

---
Summary
- From “Structured Programming” to “Structured Synchronous/Reactive Programming”
- Data-oriented and Control-oriented programming are useful and complementary, but require different approaches
  - declarative / imperative (since the '80s)
- Let's not give up on imperative programming yet!

---
Structured Synchronous Programming with Céu
(a data-oriented perspective)
Francisco Sant'Anna
    francisco.santanna@gmail.com
        @fsantanna_puc
     (I'll tweet the slides here!)
www.ceu-lang.org