Algorithms for Distributed Systems under Wireless Sensor Networks
www.ceu-lang.org

---
Overview
- Library of DS algorithms
  - topology, broadcast, leader, etc
- Wireless Sensor Networks
  - unreliable communication
  - hundreds of nodes
- Abstractions in Céu?
- Simulation in Céu?

---
Abstractions

---
Overview of Céu
- Sequences
  - … ; S1 ; S2 ; S3 ; …
- Await
  - … ; S1 ; await E1 ; S2 ; await E2 ; …
- Parallelism
  - par do
    … ; S11 ; await E11 ; S12 ; await E12 ; …
    with
    … ; S21 ; await E21 ; S22 ; await E22 ; …
    end

---
Abstractions
    par do
        … ; S11 ; await E11 ; S12 ; await E12 ; …
    with
        … ; S21 ; await E21 ; S22 ; await E22 ; …
    end
    function f1 = { S ; await E; }
    par do
        … ; S11 ; await E11 ; f1(); …
    with
        … ; f1(); S22 ; await E22 ; …
    end

---
Macros
    macro f1 = { S ; await E; }
    par do
        … ; S11 ; await E11 ; f1(); …
    with
        … ; f1(); S22 ; await E22 ; …
    end
    /************/
    par do
        … ; S11 ; await E11 ; S ; await E ; …
    with
        … ; S ; await E ; S22 ; await E22 ; …
    end

---
Macros in Céu
- Text substitution prior to Céu compilation
  - ”macro expansion”
  - GNU m4
- Advantages
  - minor changes to the language
  - Céu remains static (analysis + faster)
- Disadvantages
  - duplicates code (more memory)
  - error messages

---
   // app.ceu
    include(lib.m4)
    par do
        ALIVE(1s);
    with
        ...
    end
   // lib.m4
    define(ALIVE, `/*{-{*/
        loop do
        await $1;
        _printf(”I'm alive\n”);
        end
    /*}-}*/´)

---
   // app.ceu_m4
    par do
        /*{-{*/
    loop do
        await 1s;
        _printf(”I'm alive\n”);
    end
    /*}-}*/;
    with
        ...
    end

---
Simulation

---
I/O in Céu
- I/O events:
  - interface with the environment
   input int A;
   output int B;
- Multiple programs:
  - each run in an OS process
  - link I/O: app1 B → app2 A
  - communicate through OS queues
A
B
A
B

---
Example
send_recv.lua

---
DS algorithms

---
Fault Tolerance
- Sends are unreliable
  - never trust it
  - Example: collisions.lua
- Buffers may overflow
  - avoid use of buffers

---
#1 – Neighbours
Discovers which nodes are within range
u8[2] nodes = b0000000000000000;
DS_neighbours(nodes, n_nodes, am_type, retry)
- Sends an am_type broadcast message every retry event
- Receives am_type messages / saves src in nodes
- It never terminates!

---
#2 – Topology
Discovers the topology of the network
u8[2x16] nodes = b0000000000000000 // n0
        b0000000000000000 // n1
        ...
DS_topology_hb(nodes, n_nodes, am_type, heartbeat)
- Heartbeat algorithm
- Sends an am_type broadcast message with local knowledge
- Receives am_type messages with topology / ORs with local knowledge

---
#2 – Topology
First variation:
  DS_topology_hb_diam(nodes, n_nodes, am_type, hb, diam)
  - terminates after diam heartbeats
Second variation:
  DS_topology_hb_ack(nodes, n_nodes, am_type, hb)
  - terminates after
    - all nodes have a neighbour
    - all neighbours acknowledge

---
#3 – Broadcast
- Broadcast of messages in sequence to all network
  - single sender
  - multiple receivers
- Node broadcasts its frontier periodically to neighbours
- Node re-sends requests from neighbours
- Buffer to store received messages
  - tolerance: sender_period x buffer_size
@DS_bcast_frontier(type, len, am_type, recv, send, ms);