Structured Synchronous Programming with Céu
(a data-oriented perspective)
Francisco Sant'Anna
www.ceu-lang.org

---
Synchronous Programming
- Real-time/continuous interaction with the environment
  - I/O, sensor/actuators
- Two approaches (early 80s in France):
  - Control oriented (imperative): Esterel
  - Data oriented (functional/declarative): Lustre/Signal
- Global/external notion of time (e.g., clock ticks)
- Synchronous hypothesis
  - “Reactions execute infinitely faster in comparison to the input rate.”
- The synchronous model requires asynchronous primitives
  - take time and execute across reactions (e.g., network communication, heavy computations, etc.)

---
Synchronous Programming
- Esterel
  - Control dependency
  - Imperative statements
  - Reactive to the environment
    - Program counter
      - Synchronous: one input at a time
- Lustre
  - Data dependency
  - Equations/Combinators
  - Reactive to the environment
    - Graph traversal
      - Synchronous: complete traversal
Environment
Input
Output

---
Synchronous Programming
Can we cross this line?
Can we reconcile control and data-oriented
 synchronous programming?

---
“Hello world!” in Céu
Blinking a LED
  1. on ↔ off every 500ms
  2. stop after “press”
  3. restart after 2s
- Compositions
  - seq, loop, par (trails)
    - At any level of depth
  - state variables / communication
    par/or do
       loop do
        await 500ms;
        _leds_toggle();
       end
    with
       await PRESS;
    end
 loop do
    par/or do
       loop do
        await 500ms;
        _leds_toggle();
       end
    with
       await PRESS;
    end
    await 2s;
 end
       loop do
        await 500ms;
        _leds_toggle();
       end
Lines of execution
=
Trails (in Céu)

---
Design guidelines / Tradeoffs in Céu
(vs data streams/signals + functional combinators)
(vs ???)
(vs garbage collection)
(vs purity / immutable data)
(vs “free parallelism”)
- Control flow
  - explicit state machines (fold combinator)
- Structured programming
- Bounded execution and memory
- Automatic memory management (lexical scope + safe abortion)
- Side effects everywhere
- Sequential/Deterministic semantics (real parallelism relies on asynchronous primitives)
- Data flow
  - explicit loops with side effects
crossing the line

---
Mixing data & control
- Controlling the ball inside a rectangle
  - click the mouse to start
  - click the mouse to turn right (always)
- Data flow:
  - velocity is the integral of acceleration
  - position is the integral of velocity
- Control flow:
  - abrupt changes in the edges (non-continuous functions)
  - discontinuity imposes state machines (e.g., isRunning, curDirection)

---
Moving the ball
- Ugly, lengthy, low level!
  - simple data dependency pattern
    - 1 par + 2 loop
- Abstractions
  - Organism = Object + Trails
    - Interface (fields + methods)
    - Body (any code in Céu)

---
Moving the ball
- Organisms
  - constructor starts the body to execute in parallel with the remaining block
- Still verbose
  - Local transformations only
  - Syntactic sugar

---
Making the turn
- Doesn't work as expected
  - previous dependency still active
- Lexical scope for organisms
  - data reclaimed, body aborted
- Mixing data and control flow
  - automatic data updates
  - no explicit state machines or resets
  - structured code with lexical scope

---
Closing the loop
- Lenghty code...
  - ... but regular
  - “abstractable” with macro or class

---
Closing the loop
Structured, sequential, and with encapsulated data flow.

---
Recursive data structures
- Interpreter for a simple Logo turtle
  - move N pixels
  - rotate N degrees
  - sequence, repetition
- Program as an abstract syntax tree (AST)
  - sequence and repetition are recursive

---
Recursive data structures

---
Structured Recursive Loops

---
A more powerful Turtle
- Interpreter for a powerful Logo turtle
  - move N pixels per second
  - rotate N degrees per second
  - await N milliseconds
  - sequence, repetition, par/or

---
A more powerful Turtle

---
References
- “Real Time Programming: Special Purpose or General Purpose Languages” - G. Berry (1989)
  - synchronous model, interactive vs reactive systems
- “Preemption in Concurrent Systems” - G. Berry (1993)
  - safe abortion, Esterel semantics
- “Safe Concurrent Abstractions for Wireless Sensor Networks” - (SenSys'13)
  - static Céu, constrained platforms (8bit CPU, 4K RAM)
- “Structured Synchronous Reactive Programming with Céu” - (Modularity'15, FPW/StrangeLoop'14)
  - dynamic Céu, abstractions with lexical scope

---
Summary
- From “Structured Programming” to “Structured Synchronous/Reactive Programming”
- Data-oriented and Control-oriented programming are useful and complementary, but require different approaches
  - declarative / imperative (since the '80s)
- Let's not give up on imperative programming yet!

---
Structured Synchronous Programming with Céu
(a data-oriented perspective)
Francisco Sant'Anna
    francisco.santanna@gmail.com
        @fsantanna_puc
     (I'll tweet the slides here!)
www.ceu-lang.org

---
Extra
Slides

---
From “Structured Programming”
    To “Structured Reactive Programming”
- The await statement
  - Imperative-reactive nature
- Compositions
  - Control structures + parallels
- Synchronous execution model
  - Time ~ Sequence of events
- Esterel did this back in the '80s
- What about abstractions and modularization?
- Control Structures
  - Sequences, Loops, Conditionals
- Blocks, Scopes, Locals
  - Automatic memory management
- Subroutines
  - Abstraction mechanism
- What about reactivity?
  - Environment event → Short-lived callback
  - No more loops, scopes, etc.
  - Breaks structured programming
    - “Callbacks as our Generations' goto” [Miguel de Icaza]

---
Céu goals
Céu non-goals
Back-end infrastructure
  - High-performance servers
  - Clusters, Cloud computing
Independent sessions/actors
  - Latency in communication
  - Distribution
The C10K problem
  - Concurrency w/ Parallelism
Front-end applications
  - GUIs, Games, interactive apps
  - Desktops → Arduino (4K RAM)
Ruled by the environment
  - Immediate/real-time feedback
  - Global consensus
Logical reasoning
  - Concurrency w/ Determinism

---
Céu Organisms
Organism ~ (Object + Trails)
 class Blink do
    var int led;
    var int but;
 with
    loop do
       par/or do
        every 500ms do
        _leds_toggle(this.led);
        end
       with
        var int bt =
        await PRESS
        until bt==this.but;
       end
       await 2s;
    end
 end
 class <ID> with
    <interface>
       // properties
       // methods
 do
    <body>
       // Céu code
 end
Organisms react directly to
the environment

---
“Reactive” terminology: historical perspective
- [1985] “On the development of reactive systems”, David Harel et. al.
- [1987] “Statecharts: A Visual Formalism for Complex Systems”, David Harel
- [1989] “Real time programming: Special purpose or general purpose languages”, Gérard Berry
- [2007-HOPL] "Statecharts in the Making: A Personal Account", David Harel

---
“Reactive” terminology
- [1985] “On the development of reactive systems”, David Harel et. al.
- [1987] “Statecharts: A Visual Formalism for Complex Systems”, David Harel

---
“Reactive” terminology
[1989] “Real time programming: Special purpose or general purpose languages”, Gérard Berry

---
“Reactive” terminology
[2007-HOPL] "Statecharts in the Making: A Personal Account", David Harel

---
Reactive languages
discrete

---
Execution model
1. Programs starts in the “boot reaction” in a single trail.
2. Trails execute until they await or terminate. This step is known as “reaction chain” and always executes in bounded time.
3. An input event occurrence awakes all trails awaiting that event. Repeat “step 2”.
 par/and do
    <...> // 1
    await A;
    <...> // 3
 with
    <...> // 2
    await B;
    <...> // 4
 end
<...> are trail segments that do not await
        (e.g. atrbuições, chamadas de função)

---
Execution model
- Synchronous hypothesis: “Reactions execute infinitely faster in comparison to the input rate.”
- In theory: a program does not take time on “step 2” and is always idle on “step 3”.
- In practice: if an event occurs while a reaction takes place, the event is enqueued for the next reaction.
- Reactions to events never overlap.
- When multiple trails are active (i.e., awoken from the same event), they execute in the order they appear in the source code.

---
Bounded execution
- Céu ensures bounded execution
  - All loops must await or break
- Limitation: long computations
loop do
  if <cond> then
    break;
  else
    await A;
  end
end
loop do
  if <cond> then
    break;
  end
end

---
Shared memory
var int x=1;
par/and do
    await A;
    x = x + 1;
with
    await A;
    x = x * 2;
end
_printf(“%d\n”, x);
var int x=1;
par/and do
    await A;
    x = x + 1;
with
    await B;
    x = x * 2;
end
_printf(“%d\n”, x);
- Static analysis
  - ceu --safety 0 # allows both
  - ceu --safety 1 # allows LEFT, refuses RIGHT
  - ceu --safety 2 # refuses both

---
Organism transformation
struct _Blink with
    var int pin;
    var int dt;
end;
do
    var _Blink b1, b2;
    par/or do
        // body of b1
        b1.pin = 11;
        b1.dt = 500;
        loop do
        await (b1.dt)ms;
        _toggle(b1.pin);
        end
        await FOREVER;
    with
        // body of b2
        b2.pin = 12;
        b2.dt = 1000;
        loop do
        await (b2.dt)ms;
        _toggle(b2.pin);
        end
        await FOREVER;
    with
        await 1min;
    end
end
class Blink with
    var int pin;
    var int dt;
do
    loop do
        await (this.dt)ms;
        _toggle(this.pin);
    end
end
do
    var Blink b1 with
        this.pin = 11;
        this.dt = 500;
    end;
    var Blink b2 with
        this.pin = 12;
        this.dt = 1000;
    end;
    await 1min;
end
par/or do
    loop do
        await 500ms;
        _toggle(11);
    end
with
    loop do
        await 1s;
        _toggle(12);
    end
with
    await 1min;
end

---
Resources
- Internal
  - Céu -> C
- External
  - C -> Céu
par/or do
   var _message_t msg;
   <...> // prepare msg
   _send_request(&msg);
   await SEND_ACK;
with
   <...>
end
par/or do
   var _FILE* f = _fopen(...);
   _fwrite(..., f);
   await 1s;
   _fwrite(..., f);
   await 1s;
   _fclose(f);
with
   <...>
end
local memory
to
external pointer
external memory
to
local pointer
May terminate
May terminate
line 5 : call to "_send_request" requires `finalize´
line 2 : attribution requires `finalize´

---
Resources
- Internal
  - Céu -> C
- External
  - C -> Céu
par/or do
   var _message_t msg;
   <...> // prepare msg
   finalize
      _send_request(&msg);
   with
      _send_cancel(&msg);
   end
   await SEND_ACK;
with
   <...>
end
par/or do
   var _FILE&? f;
   finalize
      f = _fopen(...);
   with
      _fclose(&f);
   end
   _fwrite(..., &f);
   await 1s;
   _fwrite(..., &f);
   await 1s;
   _fclose(&f);
with
   <...>
end

---
Resources
- Internal
  - Céu -> C
- External
  - C -> Céu
par/or do
   var _message_t msg;
   <...> // prepare msg
   finalize
      _send_request(&msg);
   with
      _send_cancel(&msg);
   end
   await SEND_ACK;
with
   <...>
end
par/or do
   var _FILE&? f;
   finalize
      f = _fopen(...);
   with
      _fclose(&f);
   end
   _fwrite(..., &f);
   await 1s;
   _fwrite(..., &f);
   await 1s;
   _fclose(&f);
with
   <...>
end

---
par/or
- Céu in one feature
- par: lexical composition of activites
  - static reasoning, static memory
  - synchronous execution
- or: orthogonal abortion
  - safe/consistent termination
  - no need for garbage collection
- permeates all aspects of the language
  - organism expansion, reference watching, finalization

---
(Related) Observers
Use the observer pattern
  1. Create a Blink class
  2. Create two instances
  3. Add instances as listeners for timers and button events
  - Explicit references
  - No loops and parallel compositions (short-lived methods)
In some communities, the observer pattern is a synonym for
imperative reactive programming
 (even though Esterel has been around for >30 years)
- Memory (heap) management:
  - Memory leaks
  - Dangling pointers
  - Garbage collection (“lapsed listeners”)
We want something as simple as locals with automatic management!

---
(Related) Esterel
- Fundamental differences
  - A single external event defines a reaction
    - safe shared-memory concurrency
  - Stack-based execution for internal events
- Other differences
  - Finalization for resources
  - First-class timers
  - Organisms

---
(Related) Simula
- Similar syntactic structure
  - Interface + Body
- Different execution models
  - Cooperative vs Synchronous/Reactive/Independent
- Compositions
  - Single body vs Parallel compositions
- Memory management (reasoning)
  - Heap vs Lexical scope

---
“Free Parallelism”
- Two problems:
  - signals are not in-memory collections
    - (past values should have been handled, future values are not available yet)
  - state machines are inherently sequential
    - the order matters
    - (fold can only be parallel with associative accumulator functions)